## Slide 1: Satellite Operation
Noji Ratzlaff
KNØJI
noji.com/hamradio

## Slide 2: Satellites
A variety of satellite types
We’re addressing artificial satellites that orbit the Earth
More specifically, amateur radio satellites
BTW, the ISS is also a satellite

## Slide 3: Our goal
Because each satellite contains a repeater
The objective is to use a satellite to make a contact with another ham
Start by making a
dual-band antenna
Here’s the link

## Slide 4: Your tasks
Here are the steps (link to the steps):
Install the Heavens-Above app
Determine your grid square
Decide on a satellite
Collect the satellite info
Set up your radio
Rehearse the sweep
Make a contact

## Slide 5: Install Heavens-Above
There are others, but this one’s my favorite
Go to your app store and download it (free)
Start the app
Tap Radio satellites and scroll
Some list only downlink; seek both uplink and downlink
Dates and times are local 24-hour, not UTC

## Slide 6: Determine your grid square
The Earth is divided into “squares”
This website is egloff.eu/qralocator

## Slide 7: Determine your grid square
We’re in DN

## Slide 8: Determine your grid square
We’re in DN40

## Slide 9: Determine your grid square
Utah view

## Slide 10: Decide on a satellite
Start with the date
Pick one with
high elevation
both Up and Down
Note the time window

## Slide 11: Collect the satellite info
Tap SKY CHART to show the chart and window

## Slide 12: Collect the satellite info
Tap INFO to show its information
Downlink frequency
Uplink frequency

## Slide 13: Set up your radio
Not all radios can support satellite features
Must be capable of 290.960 MHz offset
Must be dual-band and dual-watch
Turn on dual-watch (TDR)
Turn off the squelch
Calculate the Doppler shift offsets in both positive and negative directions for the downlink, about 5 kHz apart
Most Baofeng HTs and Yaesu VX-8R can

## Slide 14: Set up your radio
Program eight channels as follows:

## Slide 15: Rehearse the sweep
Determine the sweep time and elevation
Divide the time into four time segments
Practice the sweep
With only the antenna
With antenna and radio
With both while switching channels
With both, switching channels, and saying
K-I-7-A-B-C, D-N-4-0
(my comma indicates a brief pause)

## Slide 16: Make a contact
Enable the satellite repeater (Channel 101 for two seconds) or if it’s already in use
Call on Channel 102 as follows:
K-I-7-A-B-C, D-N-4-0 (phonetics)
The other person replies
N-6-D-L-O, D-M-6-9 (phonetics)
You repeat and conclude (no phonetics)
roger, roger, N6DLO, thanks for DM69
Ta-dah!

## Slide 17: If you have the means
Full-scale satellite station

## Slide 18: Feel free to contact me
Noji Ratzlaff KNØJI
nojiratz@hotmail.com